1.) A thin, 80.0  disk with a diameter of 9.00  rotates about an axis through its center with 0.220  of kinetic energy.

What is the speed of a point on the rim?

2.) A 3.0-m-long rigid beam with a mass of 100 kg is supported at each end. An 80 kg student stands 2.0 m from support 1. How much upward force does support 1 exert on the beam?

3.) The 20-cm-diameter disk in the figure can rotate on an axle through its center.

What is the net torque about the axle? In Nm

4.) A 1.0 kg ball and a 2.0 kg ball are connected by a 1.0-m-long rigid, massless rod. The rod is rotating cw about its center of mass at 20 rpm.

What torque will bring the balls to a halt in 5.0 s? in Nm