Problem 1)

- An electrical manufacturing makes delta motors (X1) and Y- motors (X2). For this it has four operations –stamping , casting , wiring, and an assembly and testing.  Each unit of  a delta motor requires 2 hours in the stamping department, 3 hours in the wiring dept. and 1 hour for assembly and testing.  Each Y-motor  requires 2 hours in stamping,  3 hour in casting , 1 hour in wiring , an ½ hour for assembly & testing .  The profit (in hundreds of dollars is  3$ for a delta motor and $3.6 for a Y-motor .  The available capacity of each operation is below : (leave profit in hundreds of dollars)

Stamping  8 hours               Wiring 7.5 hours

Casting    9  hours                Assembly and testing 3 hours

Set up the LP problem , the first tableau, and solve for the objective  row and the stub in the second tableau .

b)

|  | X1 X2 | X3 X4 | X5 X6 | -P Xb |
| --- | --- | --- | --- | --- |
| X1 | 1 0 | ½ -1/3 | 0 0 | 0 1 |
| X2 | 0 1 | 0 1/3 | 0 0 | 0 3 |
| X5 | 0 0 | -3/2 2/3 | 1 0 | 0 3/2 |
| X6 | 0 0 | -1/2 1/6 | 0 1 | 0 1/2 |
| -P | 0 0 | -3/2 -1/5 | 0 0 | 1 -69/5 |

Above is the third tableau . Discuss why this is optimal and give the answers

2) Determine the range of optimality .

3) Determine the range of feasibility

4) Discuss the implication of one half an hour more time available for wiring . Back your answer with figures.

5) If you had one hour less stamping , and one hour more casting time available , what would the solution be?

6) If the profit of the delta motors dropped from $3 to $2 .50 how would this change the outcomes ?

7) Set up the dual and give its answers

Problem 2.

Use the assignment method to determine the best way to assign workers to jobs , given the cost  information below.  Compute total cost for your assignment plan.                         JOB

|  | A | B | C | D | E |
| --- | --- | --- | --- | --- | --- |
| 1 | 7 | 7 | 6 | 9 | 3 |
| 2 | 6 | 9 | 8 | 7 | 5 |
| 3 | 5 | 6 | 9 | 8 | 10 |
| 4 | 8 | 9 | 7 | 5 | 6 |

# Problem 3

Water is to be pumped from three wells to meet demands in five towns in such a way as minimize surcharge costs .  In the table below , well capacities and town demands are expressed in gallons per hour .  Determine an initial solution for the distribution of water from wells to towns.

|  |  | SURCHARGE(CENT PER 100GALLON) TOWN |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | 1 | 2 | 3 | 4 | 5 |  |
| A | 4 | 16 | 2 | 10 | 19 | 500 |
| B | 18 | 7 | 9 | 3 | 15 | 675 |
| C | 13 | 8 | 22 | 11 | 6 | 800 |
| WELL DEMAND (GPH) | 400 | 400 | 500 | 375 | 300 |  |

Use VAM ,  MODI , and stepping stone methods to calculate the least surcharge cost.

Set up the underlying linear programming problem.