E2-4 Manufacturing cost data for Copa Company, which uses a job order cost system,

are presented below.

Case A 			Case B 			Case C

Direct materials used 		$ (a) 			$ 83,000 			$ 63,150

Direct labor 			50,000 			100,000			 (h)

Manufacturing overhead applied	 42,500 			(d) 			(i)

Total manufacturing costs 		165,650 			(e) 			250,000

Work in process 1/1/05		(b) 			15,500 			18,000

Total cost of work in process 		201,500 			(f) 			(j)

Work in process 12/31/05 		(c) 			11,800			 (k)

Cost of goods manufactured 		192,300			 (g) 			262,000

Instructions

Indicate the missing amount for each letter. Assume that in all cases manufacturing overhead is applied on the basis of direct labor cost and the rate is the same.