Consider the following system whose state space representation is as follows:

x'1(t)          -3       1         x1(t)             1

=                                     +                u(t)

x'2(t)          -2     1.5        x2(t)             4

x1(t)

y(t) = [ 1   1]

x2(t)

- Show that the system is not completely controllable.

- Determine which mode is not controllable.

- Design a feedback controller such as one of the closed loop poles is located at s= -4.

- If possible, design an output feedback controller for the system.