Riding a Loop-the-loop. A car in an amusement park ride rolls without friction around the track shown in the figure    . It starts from rest at point at a height above the bottom of the loop. Treat the car as a particle.

1. What is the minimum value of (in terms of ) such that the car moves around the loop without falling off at the top (point )?

Top of Form

=

Bottom of Form

2. If the car starts at height and the radius is , compute the speed of the passengers when the car is at point , which is at the end of a horizontal diameter.

Take the free fall acceleration to be .

Top of Form

=

Bottom of Form

3. If the car starts at height and the radius is , compute the radial acceleration of the passengers when the car is at point , which is at the end of a horizontal diameter.

Take the free fall acceleration to be .

Top of Form

=

Bottom of Form

4. If the car starts at height and the radius is , compute the tangential acceleration of the passengers when the car is at point , which is at the end of a horizontal diameter.

Take the free fall acceleration to be .

Top of Form

=

Bottom of Form