A mild steel shaft (modulus of elasticity = 210 GN/m2) has a stepped circular cross-section. Part A has a diameter of 75 mm and a length of 425 mm. Part B has a diameter of 60 mm and has a length of 375 mm. The shaft carries an axial tensile load of 65.0 kN.

Determine:

- The stress in Part A

- The stress in Part B

- The strain in Part A

- The strain in Part B

- The total extension of the shaft.

# Text boxes

65.0 kN

425 mm

375 mm

65.0 kN

A

B

Ө 75 mm

Ө 60 mm