REVISION QUESTIONS

For the circuit shown below, determine the required values of RD, R1 and R2 so that the transistor operates in the saturation region with ID = 0.5mA and VD = +3V. The enhancement mode PMOS transistor has VT = -1V and K = 0.5mAV-2. What is the largest value RD can have while maintaining the transistor in saturation?

# Text boxes

R 1

R 2

R D

VDD = +5V

VD

ID