A hoist drum consists of a uniform cylinder of diameter 1.2m, radius of gyration 0.45m and mass 200kg. It is being used to lower a crate of mass of 60 kg which is attached to the hoist by a light, inextensible rope. Initially, the crate is at rest 3.0 m above the ground.

A brake on the drum is accidentally partially released and the crate accelerates uniformly, reaching the ground after 2.20 seconds.

Determine

- The linear acceleration of the crate.

- The angular acceleration of the drum.

- The tension in the cable.

- The moment of inertia of the hoist drum.

- The friction torque from the brake on the drum.

# Text boxes

Hoist

Drum

Crate