The mechanism shown in the figure    is used to raise a crate of supplies from a ship's hold. The crate has total mass 56.0 . A rope is wrapped around a wooden cylinder that turns on a metal axle. The cylinder has radius 0.310  and a moment of inertia  = 2.40  about the axle. The crate is suspended from the free end of the rope. One end of the axle pivots on frictionless bearings; a crank handle is attached to the other end. When the crank is turned, the end of the handle rotates about the axle in a vertical circle of radius 0.120 , the cylinder turns, and the crate is raised.

What magnitude of the force applied tangentially to the rotating crank is required to raise the crate with an acceleration of 0.750 ? (You can ignore the mass of the rope as well as the moments of inertia of the axle and the crank.)