a) Find the Thevenin’s circuit for the circuit shown in Fig.5.1 similar to the circuit shown in Fig.5.2.

b) Calculate the output voltage for different load resistors and the corresponding power and enter these values in Table 1:

c) Plot a graph of load resistance vs power using Matlab 7 (use semilog format as shown in Fig.5.3). Find the load resistance corresponding to the maximum power.

(use the following Matlab script to plot the graph)

% Define your load voltage and load resistance vectors here as vl and rl

vl =[ 		];

rl =[ 		];

% calculate power by the following formula

pl=vl.*vl./rl;

figure(1)

semilogx(rl, pl);

title('Maximum Power Transfer Analysis')

xlabel('Load Resistance (Ohms)');

ylabel('Power (milli watts');

grid

% You can drag the legend with the mouse to a desirable place

d) For each value of RL in Table 1, calculate the circuit efficiency using the formula: