A4

(a) Calculate the change in output code from the ADC for the transducer if the gap is changed from 500 (m to 600 (m.

(b) If the transducer was removed from the circuit what would be the DC offset voltage measured at the output.

(c) What is the bandwidth of the system response to changes in input gap?

Figure A4

Additional information:

Op-amp:	Input offset voltage	5 mV

Input bias current	1 nA

Switch SW	Charge injection	0.5 pC

Switch frequency	1 MHz

ADC		Resolution	12 bit

Sampling frequency	20 kHz

Transducer	Diameter	2 cm

Air dielectric

Note (0 = 8.854 pF/m