The industrial engineer for an ice cream chain is performing a time study to determine the standard time for serving sundaes to customers.  He times 10 cycles of the task and records the observations on the table below:

The engineer rated the pace of elements 1 and 4 (pick up cup, and hand to customer) at 100%, and the other 2 elements at 90%.  The PR&D (personal, rest, and delay) allowance is 13%.

Compute the standard of the task (servicing sundae).

Equations:

NT (normalized Time)

= ET (Elemental Time)

x RF (Rating Factor)

Standard Time = ∑NT (normalized Time) x (1 + PR&D)

|  | Cycle (times in seconds) | Total | (Avg) ET | RF | NT |
| --- | --- | --- | --- | --- | --- |
| Task | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |  |  |  |  |
| 1. Pick up cup | 1.2 | 1.5 | 1.4 | 1.4 | 1.5 | .18 | 1.9 | 1.4 | 1.3 | 1.9 |  |  |  |  |
| 2. Fill with Sundae | 9.1 | 8.9 | 9.5 | 9.7 | 8.9 | 9.5 | 9.3 | 8.8 | 10.1 | 9.2 |  |  |  |  |
| 3. Add topping | 5.7 | 5.8 | 5.4 | 5.2 | 6.0 | 5.5 | 5.8 | 6.0 | 5.4 | 6.2 |  |  |  |  |
| 4. Hand to customer | 3.2 | 3.4 | 3.8 | 3.9 | 3.2 | 3.1 | 3.5 | 3.6 | 3.4 | 3.5 |  |  |  |  |