- Suppose a router has built up the routing table shown in Table below.  The router can deliver packets directly over interfaces 0 and 1, or it can forward packets to routers R2, R3, or R4.  Describe what the router does with a packet addressed to each of the following destinations

  - 128.96.39.10

  - 128.96.40.12

  - 128.96.40.151

  - 192.4.153.17

  - 192.4.153.90

Subnet #                        SubnetMask                                         NextHop

128.96.39.0		255.255.255.128			Interface 0

128.96.39.128             255.255.255.128                              Interface 1

128.96.40.0		255.255.255.128			R2

192.4.153.0		255.255.255.192			R3

0.0.0.0  (default)	0.0.0.0				R4