Circularity of the DFT/FFT. Using the same x[n] (shown below):

a) stem(x);

b) Use the shift theorm to plot x delayed by 1, 4, 5, 6, and 8 samples, and plot the result

for each. Remember the shift theorem says a delay by t0 seconds is equal to multiplying the

spectrum by e-jΩt0. So to do this, do stem(real(ifft( exp(-j*m*t0).*fft(x))));

for the different values of t0. (the real is needed because round-off errors introduce some

imaginary values that don’t really exist. If you plot the imaginary part you’ll see it’s ~10-15).

For sequence x[n]=[1 1 1 1 0 0 0 0] for n=0:7, so N=8

plot X[ω], , where

clear all;

close all;

w=0:0.01:2*pi;

%calculated Fourier transform

Xw=(1-exp(-j*4*w))./(1-exp(-j*w));

x=[1 1 1 1 0 0 0 0];

m=(0:7)*2*pi/8;

%plot real part of Xw

plot(w,real(Xw),'LineWidth',2);

hold on;

%plot the real part of fft(x)

stem(m,real(fft(x)),'r','LineWidth',2);

xlabel('\omega','FontSize',16);

ylabel('FFT of x[n]','FontSize',16);

title('Real Part of FFT','FontSize',16);