1, the following data are taken from a certain heat transfer test. The expected correlation equation is   y=ax^ (b). Plot the data in an appropriate manner and use the method of least squares to obtain the best correlation.

| X | 2040 | 2580 | 2980 | 3220 | 3870 | 1690 | 2130 | 2420 | 2900 | 3310 | 1020 | 1240 | 1360 | 1710 | 2070 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Y | 33.2 | 32.0 | 42.7 | 57.8 | 126.0 | 17.4 | 21.4 | 27.8 | 52.1 | 43.1 | 18.8 | 19.2 | 15.1 | 12.9 | 78.5 |  |

(a) find   a0, a and da0( or square root of “a0”), da (or square root of “a”)

(b) Calculate the mean deviation of these data from the best correlation

2) for the following data points y is expected to be a power law function of x. obtain this quadratic function by means of a graphical plot and also by the method of  least squares:  function:  y=a0 X ^(a1)

| X | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- |
| y | 1.9 | 9.3 | 21.5 | 42.0 | 115.7 |

- find a0, a, square root of “a” that gives the best fit for the data.

- Plot the data