1. Gates	 Implement the 1 bit full adder using only:

- 2 input NAND gates

- 2 input NOR gates.

2. Boolean Functions

Using the laws of Boolean algebra, minimize the number of operators in the following Boolean functions:

- wy’+ wx’y + wxyz + wxz’

- abc + a’d + b’d + cd

3. Given the following truth table, write the Boolean function, simplified as much as possible. Draw the logic circuit using only 2-input AND, OR and NOT gates.

xwyz F

| 0000 | 0 |
| --- | --- |
| 0001 | 1 |
| 0010 | 0 |
| 0011 | 0 |
| 0100 | 0 |
| 0101 | 1 |
| 0110 | 0 |
| 0111 | 1 |
| 1000 | 0 |
| 1001 | 1 |
| 1010 | 1 |
| 1011 | 1 |
| 1100 | 0 |
| 1101 | 1 |
| 1110 | 1 |
| 1111 | 1 |

4. Logic Operations

Given A,B are 32 bits wide. Write the result stored in B after each one of this operations (for each line, assume B has the value assigned to it by the previous operation). Write your results using hexadecimal numbers. A = 0x12345678 (initial value)

- B = A AND 0x87654321

- B = B XOR 0x33333333

- B=BORA

- B=NOTB

- Combinational Circuits

Design a binary-to-decimal decoder whose inputs are 4-bit BCD-encoded numbers (x3x2x1x0) and whose outputs are lines (d9, d8,. . . , d0). The circuit should be minimized as much as possible.