1. S-R Latch

Given the following NAND implementation of an S-R latch,

Write its truth table.

| Qt St | Rt | Qt+1 |
| --- | --- | --- |
| 0 | 0 | 0 |  |
| 0 | 0 | 1 |  |
| 0 | 1 | 0 |  |
| 0 | 1 | 1 |  |
| 1 | 0 | 0 |  |
| 1 | 0 | 1 |  |
| 1 | 1 | 0 |  |
| 1 | 1 | 1 |  |

2. Gate S-R latch.

Given the following implementation of a gated (clocked) S-R latch and its truth table.

| S | R | C | Q | Q’ |
| --- | --- | --- | --- | --- |
| 0 | 0 | 1 | lastQ | lastQ’ |
| 0 | 1 | 1 | 0 | 1 |
| 1 | 0 | 1 | 1 | 0 |
| 1 | 1 | 1 | 1 | 1 |
| x | x | 0 | lastQ | lastQ’ |

Draw the Q output in the timing diagram:

** assume NO time delay for transitions

3. Gated D Latch.

Given the following implementation of a gated D latch and its truth table.

| CD | Q | Q’ |
| --- | --- | --- |
| 10 | 0 | 1 |
| 11 | 1 | 0 |
| 0 x | lastQ | lastQ’ |

Draw the Q output in the timing diagram:

** assume NO time delay for transitions

4. Edge triggered D Flip Flop

Given the following implementation of an edge triggered D flip flop and its truth table.

| D | Q |
| --- | --- |
| 0 | 0 |
| 1 | 1 |

Draw the Q output in the timing diagram:

** assume NO time delay for transitions