Calculate the maximum growth rate (µmax) and the specific growth rate (µ) at time=10 hours

Cell growth data:

| Time (h) | X(g/L) |
| --- | --- |
| 0 | 0.2 |
| 2 | 0.211 |
| 4 | 0.305 |
| 8 | 0.98 |
| 10 | 1.77 |
| 12 | 3.2 |
| 14 | 5.6 |
| 16 | 6.15 |
| 18 | 6.2 |

when µ is constant ln X-ln X0 = µt