Problem 1

The following circuit is left operating for a long time, until it reaches a DC steady

state.

a) Determine the DC steady state values for i1, i2, and v3.

b) Determine how much power the 24 V voltage source is supplying.

c) Calculate how much energy is stored in the 4 μF capacitor, the 20 mH inductor,

and the 10 μF capacitor.