1. Convert the following numbers to SI:

- 56.8 in  =

- 1 year =

- 34.8 atm =

- 8.3 Btu/min =

- 38.96 ft/min

- 98.6 furlongs per fortnight

- 34.5 in pdl

- 15.8 gal/min

2. Perform the following conversions:

- 34.589 Pa to psia

- 34.6 m/s to mph

- 89.6 L to m3

- 68.4 in3 to ft3

- 964 slug to lbm

- 569 pdl to lbf

- 56.8 glug to g

- 78.5 mug to kg

- 358 atm L to Btu

- 1.2 steradians to square degrees

3. Convert the following temperatures to the Kelvin temperature scale:

- 259.6(R

- 145(C

- 98.6(F

4. Convert the following temperature intervals to Kelvin.

- 58.3 C(

- 89.7 F(

- 4.5 R(

5. A weir is a slot in an open channel with water flowing over it (Figure 14.12). For a weir with a rectangular shape, the following formula can be derived:

Q = 5.35 Lh3/2

Where

Q = water flow rate. ft3/s

L = length of weir, ft

h = height of liquid above weir gate, ft

Do the following:

- Determine the units associated with the constant that are needed to make the equation dimensionally homogeneous.

- Determine a new constant that allows the following units to be used:

Q = water flow rate, gal/min

L = length of weir, ft

h = height of liquid above weir gate, in