12

.  EMF in a Bullet. At the equator, the earth's magnetic field is approximately horizontal and is directed toward the north and has a value of .

Part A

Estimate the emf induced between the top and bottom of a bullet shot horizontally at a target on the equator if the bullet is shot toward the east. Assume the bullet has a length of 1 cm and a diameter of 0.4 cm and is traveling at 300 .

Top of Form

|  |  | V |
| --- | --- | --- |

Bottom of Form

Part B

Which is at higher potential, the top or bottom of the bullet?

Top of Form

|  | the top of the bullet the bottom of the bullet |  |  |
| --- | --- | --- | --- |

Bottom of Form

Part C

What is the emf if the bullet travels south?

Top of Form

|  |  | V |
| --- | --- | --- |

Bottom of Form

Part D

What is the emf induced between the front and back of the bullet for any horizontal velocity?

Top of Form

|  |  | V |
| --- | --- | --- |

Bottom of Form

3. At the instant when the current in an inductor is increasing at a rate of 6.35×10−2 , the magnitude of the self-induced emf is 1.65×10−2 .

Part A

What is the inductance of the inductor?

L = (1.65*10^-2)/(6.35*10^-2) =0.26 H

Part B

If the inductor is a solenoid with 405  turns, what is the average magnetic flux through each turn when the current is 0.725 ?