1.     Methane has the chemical formula CH4. If the value of the Universal Gas Constant is 8.314 kJ kg-1 K-1, calculate the value of the gas constant for methane.

2.     A piston/cylinder system has an initial volume of 0.1 cubic metre and contains air at a pressure of 1 bar.   The piston compresses the air to a volume of 0.05 cubic metre. Calculate the final pressure:

- for adiabatic compression

- for isothermal compression

ASSUME Y = 1.4