Failsafe Electronics Corporation manufactures four products. Each of the products must pass through the following departments: wiring, drilling, assembly, and inspection. Time requirements in each department (in hours) for each unit produced and unit profit are summarized in the table below:

|  | Department |  |
| --- | --- | --- |
| Product | Wiring | Drilling | Assembly | Inspection | Unit Profit |
| XJ201 | 0.5 | 3 | 2 | 0.5 | $9.00 |
| XM897 | 1.5 | 0.5 | 4 | 1.0 | $12.00 |
| TR29 | 1.5 | 1 | 1 | 0.5 | $15.00 |
| BR788 | 1.0 | 2 | 2 | 0.5 | $11.00 |

Failsafe must produce at least the following:

| Product | Minimum Production |
| --- | --- |
| XJ201 | 150 |
| XM897 | 100 |
| TR29 | 300 |
| BR788 | 400 |

Production time available each month are as follows (in hours):

| Department | Capacity (in hours) |
| --- | --- |
| Wining | 1,500 |
| Drilling | 2,350 |
| Assembly | 2,600 |
| Inspection | 1,200 |

- Find the monthly production plan that maximizes profit. Non-integer answers are acceptable for planning purposes.

- Create at least one one-way SolverTable and one two-way SolverTable. You will need to analyze the solution to determine which variables to use in these tables. There are not right or wrong variables to choose but you will want to vary things that give you insight to the problem and your recommendation.

Hint: The maximum profit of the optimal solution is $16,400.

Maximum Profit = $16,400

Include at least 1 one-way and 1 two-way SolverTable.