1. A function is continuous but its first derivative has a finite discontinuity at the origin. What is your estimate of the rolloff rate?

A) 1/ƒ

B) 1/ƒ2

C) 1/ƒ3

D) ƒ2

2. A system is characterized by a transfer function. What is the natural response of the circuit?

H(s) = 1 / s+5

A) h(t) = e^5t

B) h(t) = 5e^t

C) h(t) = e^-5t

D) h(t) = sin 5t

3. As the frequency of a signal increases:

A) The resistance of a capacitor increases.

B) The resistance of a capacitor decreases.

C) The resistance of a capacitor is unaffected.

D) The capacitor becomes purely reactive.

4. If a function is even, then its Fourier transform can be written as:

A) 
B) 
C) 
D)

5. The function x(t) = A cos t sin 2t is an even function.

A) True

B) False

6. What kind of circuit is equivalent to Z = 10 + j30?

A) A 10H resistor in series with a j30H capacitor.

B) A 10H resistor in series with a j30H inductor.

C) A 10H resistor in parallel with a j30H inductor.

D) A 10H resistor in parallel with a j30H capacitor.

7. A function with impulses has no rolloff.

A) True

B) False

8. A system is characterized by a transfer function. What is the natural response of the circuit?

A) h(t) = e5t
B) h(t) = 5et
C) h(t) = e-5t cos 2t
D) h(t) = e-5t sin 2t

9. As the frequency of a signal increases:

A) The resistance of an inductor increases.

B) The resistance of an inductor decreases.

C) The resistance of an inductor is unaffected.

D) The inductor becomes purely reactive.

10. If  , are there any poles? Is the system stable?

A) No, it is not stable.
B) Yes, it is impulse stable, pole at +3.
C) Yes, it is impulse stable, pole at -3.
D) Yes, it is impulse stable, pole at 0.

11. The voltage across a 10 ohm resistor is v(t) = 100 sin (50t + 20°). Find the current and write it in phasor notation.

A) I = 100 20

B) I = 10 20

C) I = 1000 20

D) I = 10 -20

12. A rectangular pulse of height H is defined for -A/2 < t < A/2. Find the frequency domain representation X(ƒ).

A) 
B) 
C) 
D)

13. A system is characterized by a transfer function.  It is excited by a signal ƒ = cos 2t. What is the response function of the circuit in the s domain?

A) 
B) 
C) 
D)