Problem:

A mixture of benzene and toluene containing 40 mole % of benzene is to be separated to give a product of 90 mole % of benzene at the top and bottom product with not more than 10 mole % of benzene. Using an average value of 2.4 for the volatility of benzene relative to toluene, calculate the number of theoretical plates required at total reflux. Also calculate the minimum reflux ratio, if the feed is liquid and at its boiling point.