You are to design a Flat pulley drive for a refrigeration system with the compressor pulley diameter being 450mm and the motor pulley diameter being 200mm. The two shafts will be 1.95m apart and connected to a closed belt. Find

  - The angle of contact /angle of lap for the two pulleys

  - Find the required length of belt

  - Select a suitable belt and, ignoring the elongation at fitting but using the guide mass/unit length, calculate the power transmitted  if the maximum permissible tension is 1kN and the coefficient of friction is 0.25 if the motor rotates at 1450rpm

  - Also find the minimum initial tension require at commissioning stage