Systems Engineering B

### The shape of the hull of a small barge of width w, length l and depth d, can be approximated by the multivariable function f(x,y), where:

(a)	Show via multiple integration that the volume V of the hull is given by the following expression:

(b)	If the mass of the barge is 100 tonnes, and its sides must clear the water by at least 1 m to safeguard against sinking, what is the maximum payload of the vessel, to the nearest 100 tonnes?

## Vessel dimensions:	w=6m

l=20m

d=9m