Determine the location of the centroid yc, measured from the bottom, for a beam with the cross section shown in the figure.

0.5 in

2.5 in

3.0 in

5.0 in

Determine the maximum flexural stress produced by a resisting moment Mr of +5000 ft*lb if the beam has the cross section shown in the following figure. Note: I = 136 in.**4.

183 psi C

1.32 ksi T

2.21 ksi T

2.21 ksi C

A timber beam is simply supported and carries a uniformly distributed load w of 360 lb/ft over its entire 18-ft span. If the beam has the cross section shown in the following figure, determine the maximum horizontal shearing stress in the beam. Note: yc = 2.333 in., INA = 108.0 in.**4, and QNA = 26.89 in.**3.

80.7 psi

101 psi

202 psi

404 psi