A machine tool having a mass of 1000 kg and a moment of inertia J = 300 kg-m2, is supported on elastic supports with stiffnesses and locations shown.

    - Find the natural frequencies of the machine tool.

    - what are the corresponding amplitude ratios?

For i ), which one is correct answer:

        - 35.63 rad/s, 41.17 rad/s

        - 58.70 rad/s, 62.37 rad/s

        - 41.17rad/s, 57.82 rad/s

        - 70.58 rad/s, 82.37 rad/s

For ii ), which one is correct answer:

        - -2.383, 0.185

        - -5.348, 0.056

        - -7.242, 0.024